## Slide 1: Hardware Accelerated Networking for Data Center and Distributed Machine Learning
Yongqiang Xiong
Joint work with Ran SHU, Peng CHENG, Guo CHEN, Zhiyuan GUO, Lei Qu, Derek Chiou, Thomas Mochibroda
2019-08-17
Microsoft Research Asia
Microsoft Research

## Slide 2: Background: Server-centric Computing
Resources bound/shared/clustered: relying on server CPU/memory
Can we make resources independent from servers?
Notes: With the computing paradigm shifting to data centers, we see more and more computing and storage devices emerging, such as CPU, FPGA, SSD, GPU, but currently resources are bound with servers, shared and clustered with the dependency of server CPU and memory. This introduces non-trivial cost to servers, especially for many machine learning tasks, for example, GPU need to load training data from NVMe SSD, and exchange gradients with other GPUs, but nowadays, most of them need to pass through server CPU or memory, and its quite costly, So our question is, can we make the resources independent from servers?

## Slide 3: Vision: Break Server Boundary in Cloud
Everything visible and directly accessible on unified Flat network
  Global resource naming, routing, and communication.
  Harmonize data center networking (Ethernet) and host-area networking (PCIe)
Everything managed and divided dynamically by Cloud
  No boundaries & dependency from individual servers
NVMe
ACC Card
NIC
FPGA
APU
GPU
CPU
Host Switching (unified Ethernet + PCIe)
Server1
NVMe
ACC Card
NIC
FPGA
APU
GPU
CPU
Host Switching (unified Ethernet + PCIe)
Server2
NVMe
ACC Card
NIC
FPGA
APU
GPU
CPU
Host Switching (unified Ethernet + PCIe)
ServerN
Data Center Networking Fabrics (RDMA/Ethernet)
Unified Network
Notes:   Our vision is to break server boundary in the cloud, so every resource is addressable and directly accessible on the unified flat network, this needs global …
  And every resource should be managed and divided/assembled dyna

## Slide 4: One Step Further Beyond Microsoft SmartNIC
Notes: We all know about the Microsoft SmartNIC, that’s a bump-in-wire solution mainly targeting at networking virtualization with generic flow table offloading. Our proposal is a step further

## Slide 5: Proposal: Terminus as the “Server Center”
All Resources partitioned, virtualized and connected by Terminus hardware
  CPU, DRAM, storage, NIC, GPU, FPGAs, AI ASICs
  Future-device proof with programmable adaptors
Challenges
  Unified interconnection layer
    Leveraging existing infrastructure
    Global and heterogeneous dev-to-dev collaborations
    Direct universal access to interconnect cloud resources
  Super high efficiency
    High switch capacity/bandwidth
    CPU-bypass and host-memory-bypass
  Provide fine-grained hardware QoS
GPU
GPU
FPGA/
Brainslice
CPU
Memory
SSD
SSD
CPU
Memory
M.2
M.2
M.2
SSD
Terminus NIC
Switch
SOS
SOS
SOS
SOS
FPGA
SOS
SOS SOS
SOS
SOS SOS
SOS
SOS: SiliconOS
SoC
Notes: FPGAs started to replaced CPUs in MS Cloud servers for some tasks in 2015

## Slide 6: Traditional 5-layer, again…
Credit-based Host Internal Protocol
Stateless Transport /
QCQCN + PFC
MP-RDMA
SiliconTransport
Reliable Transport
NSDI 18
G-LANE
Stack
GPU
Stack
FPGA
Connect
NVMe Stack
DMA
Engine
NIC
Stack
SiliconStack
Network Stack
Underlay Stack
Passive Device
Computation Node
Communication Component
CPU
GPU
FPGA
NVMe
Memory
NIC
On-chip
NIC
SiliconOS
Hardware resource
Hardware/Network/Application Logic Interface, local memory, dev mgmt., libraries
Unified FPGA OS
Direct Universal Access (DUA) for SiliconOS through network
SiliconNet
Universal Switch
NSDI 19
SiliconInterface
Unified Interface
Generic LANE(G-LANE)
FPGA Interface
GPU Interface
MPI
ONGOING
IN PLAN
FINISH
Application
Virtualization
Docker
VM
Storage
RocksDB
Machine Learning
AIPre
H.W. Scheduler
H.W.
PS

## Slide 7: Today’s Focus
Credit-based Host Internal Protocol
Stateless Transport /
QCQCN + PFC
MP-RDMA
SiliconTransport
Reliable Transport
NSDI 18
G-LANE
Stack
GPU
Stack
FPGA
Connect
NVMe Stack
DMA
Engine
NIC
Stack
SiliconStack
Network Stack
Underlay Stack
Work with Bing
Passive Device
Computation Node
Communication Component
CPU
GPU
FPGA
NVMe
Memory
NIC
On-chip
NIC
SiliconOS
Hardware resource
Hardware/Network/Application Logic Interface, local memory, dev mgmt., libraries
Unified FPGA OS
Direct Universal Access (DUA) for SiliconOS through network
SiliconNet
Universal Switch
NSDI 19
SiliconInterface
Unified Interface
Generic LANE(G-LANE)
FPGA Interface
GPU Interface
MPI
ONGOING
IN PLAN
FINISH
Application
Virtualization
Docker
VM
Storage
RocksDB
Machine Learning
AIPre
H.W. Scheduler
H.W.
PS

## Slide 8: Direct Universal Access
FPGA 1
Server
QSFP
DDR
Server
LTL
DDR access
FPGA Connect
Host
DMA
PCIe Gen3
DDR
App 2
LTL
DDR access
FPGA Connect
Host
DMA
Datacenter networking fabric
QSFP
FPGA 2
DDR
FPGA Connect
DDR access
Host DMA
PCIe Gen3
PCIe Gen3
CPU
DUA
DUA
App 1
DUA
Intra-server networking fabric
③
②
①
④
FPGA 3
Notes: To address these problems, we propose DUA.
I first use an example to show how DUA works.
In this example, application 1 want to send a message to application 2 running on a remote server’s FPGA.
It first send the message to DUA on FPGA 2.
DUA system finds that this FPGA board does not have an Ethernet port.
It forwards this message to FPGA 1 in the same server which has Ethernet port.
Then the DUA forward this message to FPGA 3 through Ethernet.
Finally the message reaches application 2.

## Slide 9: DUA Overview
FPGA
Server
QSFP
DDR
Server
App
App
LTL
DDR access
FPGA Connect
Host
DMA
PCIe Gen3
DDR
App
App
LTL
DDR access
FPGA Connect
Host
DMA
Datacenter networking fabric
QSFP
FPGA
DDR
FPGA Connect
DDR access
Host DMA
PCIe Gen3
PCIe Gen3
CPU
DUA
DUA
App
App
DUA
Intra-server networking fabric
③
②
①
④
DUA is an “IP layer”
An abstract overlay network
Leverage all existing h/w stacks
Hierarchical addressing & routing
Notes: From the previous example, we can see that DUA is an IP layer for FPGAs to access all resources in data center.
DUA connects stacks and applications as a router and builds an abstract overlay network to unify all access.
DUA leverages existing communication stacks and can adopt future ones.
DUA doesn’t break the data center network but leverages existing address and routing design. This makes DUA simple and easy to deploy.

## Slide 10: DUA Overview
FPGA
Server
QSFP
DDR
Server
App
App
LTL
DDR access
FPGA Connect
Host
DMA
PCIe Gen3
DDR
App
App
LTL
DDR access
FPGA Connect
Host
DMA
Datacenter networking fabric
QSFP
FPGA
DDR
FPGA Connect
DDR access
Host DMA
PCIe Gen3
PCIe Gen3
CPU
DUA
DUA
App
App
DUA
Intra-server networking fabric
DUA is an “IP layer”
③
②
①
④
Efficient Routing
Direct resource access by FPGA, totally bypass CPU
Notes: DUA enables every application to access any resource in datacenter directly, no proxy application is needed.
Besides that, all the routing totally bypass CPU which provides extremely low latency.

## Slide 11: DUA Overview
FPGA
Server
QSFP
DDR
Server
App
App
LTL
DDR access
FPGA Connect
Host
DMA
PCIe Gen3
DDR
App
App
LTL
DDR access
FPGA Connect
Host
DMA
Datacenter networking fabric
QSFP
FPGA
DDR
FPGA Connect
DDR access
Host DMA
PCIe Gen3
PCIe Gen3
CPU
DUA
DUA
App
App
DUA
Intra-server networking fabric
③
②
①
④
Compatible BSD-socket Interface
for both applications and communication stacks
Efficient Routing
DUA is an “IP layer”
Notes: DUA provides a unified BSD-socket-like interface for all FPGA applications to access heterogeneous endpoint in datacenter which significantly reduce the programming effort.
Communication stacks development can also benefit from the unified interface.

## Slide 12: DUA Overview
FPGA
Server
QSFP
DDR
Server
App
App
LTL
DDR access
FPGA Connect
Host
DMA
PCIe Gen3
DDR
App
App
LTL
DDR access
FPGA Connect
Host
DMA
Datacenter networking fabric
QSFP
FPGA
DDR
FPGA Connect
DDR access
Host DMA
PCIe Gen3
PCIe Gen3
CPU
DUA
DUA
App
App
DUA
Intra-server networking fabric
③
②
①
④
Efficient Routing
Compatible BSD-socket Interface
General Multiplexing
for both applications and communication stacks
DUA is an “IP layer”
Notes: DUA provides general multiplexing for applications and communication stacks.
Programmers need to care about implementing multiplexer anymore.

## Slide 13: DUA Overview
FPGA
Server
QSFP
DDR
Server
App
App
LTL
DDR access
FPGA Connect
Host
DMA
PCIe Gen3
DDR
App
App
LTL
DDR access
FPGA Connect
Host
DMA
Datacenter networking fabric
QSFP
FPGA
DDR
FPGA Connect
DDR access
Host DMA
PCIe Gen3
PCIe Gen3
CPU
DUA
DUA
App
App
DUA
Intra-server networking fabric
③
②
①
④
Efficient Routing
Compatible BSD-socket Interface
Compatible BSD-socket interface
DUA is an “IP layer”
Unified Multiplexing
Security
Protect against both inside and outside attacks
Notes: DUA not only protects FPGA applications and stacks from outside malicious traffic, it can also protect the hosting server and even data center network from anomalous FPGA applications and stacks.

## Slide 14: System Architecture
App
FPGA
App
App
NIC
FPGA
CPU
FPGA
NIC
CPU
Datacenter networking fabric
Intra-server networking fabric
QSFP
DUA Underlay
PCIe Gen3
DDR
Server
Server
CPU Control Agent
DUA
Overlay
FPGA Control Agent
FPGA Host Stack
NVMe Stack
LTL
FPGA Connect
Host DMA
DDR Controller
DUA
data plane
DUA Data Plane
Notes: This block diagram shows the DUA system architecture.
Since FPGAs are not suitable for implementing the complicated control logic. Data plane and control plane are separated in DUA.
DUA data plane lies in all FPGAs as a router.
It provides efficient routing, unified interface, general multiplexing and security.

## Slide 15: System Architecture
App
FPGA
App
App
NIC
FPGA
CPU
FPGA
NIC
CPU
Datacenter networking fabric
Intra-server networking fabric
QSFP
DUA Underlay
PCIe Gen3
DDR
Server
Server
CPU Control Agent
DUA
Overlay
FPGA Control Agent
FPGA Host Stack
NVMe Stack
LTL
FPGA Connect
Host DMA
DDR Controller
DUA Data Plane
DUA
control plane
Notes: DUA puts the main control logic in the CPU.
FPGA control agents only monitor and update the local status.
Each server has a CPU control agent to determine all control logic within this server.

## Slide 16: DUA Control Plane
Challenge: large-scale resource and routing info dissemination
  Limited h/w resource
DUA solution
  Hierarchical addressing
  Hierarchical routing
  Leverage existing infrastructure
Fully distributed and lightweight
  Need no global synchronization
Resource table
Interconnection table
Notes: While for the data center wide, DUA control plane is organized in a distributed way.
Each CPU only maintain its local resource and routing information.
In order to realize this idea. DUA use a hierarchical address format. It leverages the server IP address as first level and let each CPU control agent manages its local address as second level.
For routing calculation, the idea is similar. Each server only manages its local routing. For cross server communications, both side’s CPU control agent calculate the intra-server routing path and leverage data center routing to build the end-to-end route. By this design, DUA avoid global synchronization.

## Slide 17: DUA Data Plane
Overlay
  Unified interface
  Routing
Stacks
  Leverage all the existing (or adopt future) stacks
Underlay
  Efficient multiplexing
  Security
App
FPGA
App
App
DUA data plane
FPGA Host stack
NVMe Stack
LTL
FPGA Connect
Host DMA
DDR Access
QSFP
DUA underlay
PCIe Gen3
DDR
DUA
overlay
Notes: Data plane consists of three parts. The overlay connects all application and stacks with unified interface and provide routing among all connected end points. This design also solves the stack multiplexing problem.
DUA leverages all existing or adopt future stacks.
The underlay solves the physical interface multiplexing and provide security check.

## Slide 18: DUA Data Plane – Overlay
Efficient & extensible design
  Switch fabric
    High capacity cross-bar switch
  Connector
    All cached routing tables
  Translator
    Protocol translation
High performance data path
  Line-rate
  Near zero-delay
DUA
overlay
LTL
DDR
FPGA Connect
Host DMA
Connector
Connector
Connector
Connector
App
App
Switch Fabric
Connector
Connector
LTL Translator
DDR Translator
Host DMA Translator
FPGA CA
App
Connector
Notes: Let’s go deeper into the overlay.
In the center is a crossbar switch that switches messages between stacks and applications.
All routing tables are cached in data plane to ensure all data transmission totally bypass CPU.
To avoid the contention during table lookup. Each connector keeps its own routing table.
Only the active connections related to a connector is cached in the table, thus the table size can be very small.
Since existing communication stacks all have their own interface. DUA adds stack translators to convert between interfaces.
Translators are carefully implemented to provide line-rate and near zero-delay.

## Slide 19: Evaluation – efficiency
Extreme low latency (< 50 ns/fwd)
FPGA 1
FPGA 4
FPGA 2
FPGA 3
APP
APP
DUA overlay
DUA overlay
FPGA Connect
FPGA Connect
LTL
LTL
FPGA Connect
FPGA Connect
Chart: Packet Size (B)
| 64 | 128 | 256
DUA | 0.15258 | 0.17625 | 0.19636
LTL | 1.266 | 1.266 | 1.316
FPGA Connect | 2.4436 | 2.4792 | 2.5448
Round Trip Time through FPGA Connect and DUA for 4 times, LTL twice
Notes: Here we use an experiment to show DUA efficiency.
We connect two FPGAs located in different servers. Both FPGAs do not have Ethernet port. DUA route traffic through other FPGAs with Ethernet for this communication.
The entire round-trip passes PCIe for 4 times, Ethernet for twice and DUA for 4 times.
The round-trip time breakdown is shown in the bottom figure.
DUA only introduces less than 200 ns latency which is less than 5% of total latency.
And for each forwarding, DUA only cause less than 50 ns.

## Slide 20: Evaluation – Logic Overhead
DUA Overlay
2 Ports: 4.24%
4 Ports: 9.29%
8 Ports: 19.86%
DUA Underlay
4 Stacks and 3 PHY Interfaces: 0.25%
Notes: Providing such low latency, DUA only introduces low FPGA logic overhead in our middle-end FPGA.
A typical 4 ports DUA implementation only consumes about 10 percent of FPGA logic resources.
These numbers will be significantly reduced by 2-3 times on the next generation FPGA.

## Slide 21: Application: Terminus for AI

## Slide 22: Application: Terminus for AI Acceleration
AI Preprocessing
NVMe SSD
Data Load
Decode
Transform
AI Training
Windows Driver
User
Kernel
Existing
Terminus
AI Preprocessing
NVMe SSD
Glane Library
Data Load
AI Training
Kernel
User
Terminus
Decode
Transform
AI-Pre

## Slide 24: Application: Terminus for AI Acceleration
Chart: Training Throughput
| 1*P100 | 2*P100
Existing | 2408.06 | 4217.56
Terminus | 2504.65 | 4531.58
Remove Software I/O Bottleneck
Platform: NVCaffe, Neural Network: AlexNet, Batch Size: 256 images, I/O Thread: 12 threads / GPU
Chart: CPU Cost
| Tradition | AI-Pre | Tradition | AI-Pre
Training | 1.09 | 1.1 | 2.64 | 2.67
IO & Pre | 7.74 | 0.56 | 18.83 | 0.83
1*P100
2*P100
Save >7 Cores per GPU

## Slide 25: AI Application #2 – Deep Crossing
45.28% Latency Reduction
Single FPGA Board: Parall = 32, 2 FPGA Board: Parall = 64
Notes: Deep crossing is a deep neural network proposed for handling web-scale application and data sizes.
The model trained from the learning process is deployed in Bing.
The critical metric is latency since it impacts service response time.
By using DUA, we easily extend the application from single board to multiple boards and doubled the parallel degree.
It only incurs 26 extra lines of OpenCL code to call the DUA interface to connect the two FPGA boards.
It result in 45 percent latency reduction which greatly improve user experience.

## Slide 26: Conclusion
Terminus: Hardware Accelerated Networking in Data Center
  Break the server boundary
  Benefits to both public and private cloud
Direct Universal Access
  Build the “IP” layer for hardware networking in data center
  In process of open source…
Hardware Accelerated Networking for Distributed Machine Learning
  AI acceleration for disk/network I/O, instead of offloading the ML algorithms
Notes: To conclude this talk.
Current FPGA communication architecture does not provide universal access to resources.
We propose DUA as the “IP” layer of FPGA communication which provide efficient routing, unified interface, general multiplexing and security.
We will open source soon.

## Slide 27: backup

## Slide 28: Benefit
Public Cloud Efficiency
  High resource utilization
    VM dynamically assembled from data center resources
    Azure Billable Utilization < 70%; Actual Utilization < 10%
  Global direct access without CPU involvement
    Harmonize data center (Ethernet) and host-area (PCIe) network
Private Cloud Characteristics
  Bare metal performance and predictability
    Avoid Noisy Neighbors for Disk Access, I/O Unfairness, etc.
  Security: minimize side channel attacks
Noisy Neighbors for Disk Access: 10ms  225ms[1]

## Slide 29: Application – Regex Matching
Up to 105~107 higher than CPU, Up to 105 lower than CPU
Up to 3 times throughput and up to 55% latency reduction compared to using CPU to move data between FPGAs
Chart: Input String Length (Byte)
| 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384
through FPGA Connect | 0.05273 | 0.10454 | 0.21062 | 0.41293 | 0.83114 | 1.6006 | 2.9905 | 4.1196 | 4.1433
through CPU | 0.018146 | 0.036212 | 0.070499 | 0.14296 | 0.27756 | 0.53776 | 0.9926 | 1.6621 | 2.4886
Pure CPU | 1.369e-05 | 9.3952e-06 | 7.382e-06 | 5.2345e-06 | 3.8923e-06 | 3.087e-06 | 4.0265e-07 | 1.3422e-07 | 2.6844e-07
Chart: Input String Length (Byte)
| 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384
through FPGA Connect | 4.4547 | 5.2886 | 6.9207 | 10.1956 | 16.7535 | 29.8323 | 56.0472 | 108.4599 | 216.9197
through CPU | 9.9627 | 10.9777 | 12.9704 | 16.8189 | 24.6383 | 40.284 | 71.5432 | 134.14 | 259.8926
Pure CPU | 502.1543 | 1465.584 | 3715.2316 | 10507.1486 | 27928.3246 | 70780.922 | 1027889.4259 | 7652668.3355 | 8611469.6478
Notes: Regular expression matching is widely used in application gateway and IDS inside data center. We use FPGA to accelerate the matching computation by several magnitudes.
However current acceleration need to use CPU to move data between FPGAs. With DUA support, data can be sent directly through FPGAs. We further reduce the latency by half and improve the throughput up to 3 times.