## Slide 1: Towards Stateless RNIC for Data Center Networks
Pulin Pan
Guo Chen
Xizheng Wang
Huichen Dai
Bojie Li
Binzhang Fu
Kun Tan
Hunan University
Huawei
Notes: Hello everyone, my name is Guo Chen. I’m an Associate Professor from Hunan University. Today I’m going to talk about ... This is a joint work with ...

## Slide 2: RDMA background
RDMA is becoming prevalent in DCN
  Low and stable latency, e.g., < 10us; High throughput, e.g. , 100Gbps; Low CPU overhead
  Widely deployed in companies such as Microsoft, Alibaba, ByteDance
Network stack in NIC
  Processing in dedicated NIC hardware
  Bypass kernel
  Zero copy
Notes: To address this problem, RDMA hardware stack is becoming prevalent in DCN.
Compared to TCP/IP, RDMA offers very low and stable latency, high throughput, and very low CPU utilization. With such high-performance, RDMA has been widely deployed in DCN such as in Microsoft.
Actually, the ultra-performance of RDMA comes from implementing the whole network stack in the NIC. As such, the stack processing is done by dedicated high-performance NIC hardware, without involving CPU and OS kernel (which contributes the most performance variance), and directly send/receive data from/to application buffer through NIC.

## Slide 3: Uniqueness of RDMA stack
Network stack on RDMA NIC (RNIC)
  Maintain massive connection-related states on RNIC
    Memory-access related
      page size, WQ length, …
    Networking related
      congestion window, recv next, IP address, …
e.g., MLX maintains 256B states for each RDMA connection (/include/linux/mlx4/qp.h mlx4_qp_context)
Still growing…
Notes: However, the side-effect of offloading network stack on NIC is that we have to maintain massive states on RDMA NIC for stack processing.
Specifically, for each RDMA connection, the NIC needs to maintain memory-access related states, including page size, WQ length, etc., and networking related states, such as congestin window, recv next sequence, IP address.
This figure illustrates the states that an RDMA NIC needs to maintain for stack processing for one connection. In practice, an RDMA connection is operated based on a queue pair, and its states are wrapped in a data structure called queue pair context. Such queue pair context is growing larger and larger, as the stack functionalities become more complicated, for example, for MLX4, the QP context is 256B.

## Slide 4: States on RNIC limit the scalability
NIC on-chip memory is scarce (e.g., several Mbs)
  Serves as a cache for connection states
Conn States
RNIC
Host memory
Conn States
Conn States
Conn States
…
Send out
Receive data/ACK
Fetch through PCIe
Performance drops when # of concurrent connections grows
  State miss on RNIC
  Fetch states from host memory
    PCIe latency becomes bottleneck
Notes: While offloading network stack gives RDMA ultra-high-performance, the connection states limit RDMA NIC’s scalability.
Specifically, different from the DRAM on the host, the NIC on-chip memory is very scarce. Therefore, the NIC memory often serves as a cache for connection states. And the whole states of all connections are stored in the host memory when there are too many connections for the NIC memory.
Consequently, the RDMA NIC performance drops a lot when there are too many concurrent connections. Specifically, many connections states are missed on the NIC. When receiving or sending data belong to those connections whose states are not on the NIC, the NIC has to fetch states from the host memory, typically through PCIe bus. Before the states have been fetched, the stack processing needs to stall since it does not know how to process. Under such condition, the PCIe latency becomes the performance bottleneck.
This figure shows our measurement results on MLX4 100G RDMA NIC. We use multiple client RNICs WRITE to one server RNIC using multiple concurrent connections. Results show that when the # of concurrent connections grow beyond 280, the overall throughput drops dramatically, and converge to only about ¼ of the maximum throughput. Meanwhile, we monitored on the server’s PCIe bus and find the number of PCIe read events suddenly grows. This verifies that the NIC is frequently fetching states from the host memory.

## Slide 5: Current status
Applications require high performance under high concurrency, e.g.,
  Distributed machine learning
    Parameter servers exchange parameters with many worker nodes
  Web-search back-end services
    Result-aggregators aggregates results from many document-lookupers
Existing works try to avoid/mitigate the impact of the RNIC scalability issue, requiring careful and constrained usage of applications
  Using large memory pages [1], connection grouping [2], or unreliable datagram [3], …
[1] FaRM: fast remote memory, NSDI 2014
[2] Scalable RDMA RPC on Reliable Connection with Efficient Resource Sharing, EuroSys 2019
[3] FaSST: Fast, Scalable and Simple Distributed Transactions with Two-Sided (RDMA) Datagram RPCs, OSDI 2016
Can we directly solve this RNIC scalability problem?
Notes: Now we know that RNIC has performance problem under high concurrency, which is due to connection states miss.
But, current applications do require RNIC has high performance under high concurrency.
To name a few such applications, for example, distributed machine learning system is very popular now. In such systems, the parameter servers need to frequently exchange parameters and gradients with many worker nodes. The communication speed is very critical to the whole system’s performance.
Another example, in web-search back-end services, a search task is distributed to many document lookup nodes. The lookup nodes concurrently search the result, and then the results are collected and aggregated by a few aggregator nodes, then rendered to the user. In such architecture, the aggregator needs to communicate with many lookup nodes efficiently.
Therefore, when applying RDMA for these application, the applications have to be very careful and often have very constrained usage on the RDMA verbs, thus to avoid or mitigate the impact of the RNIC scalability issue. For example, to support multiple connections, they use large memory pages, xxx, or even.
But till now, the RNIC scalability problem has not been solved.
In this work we try to directly tackle the problem

## Slide 6: StaR: Towards stateless RNIC
Moving states to the other communication side
  Maintain zero connection-related states, while all the RDMA data plane processing is still done by NIC hardware
Utilizing asymmetric communication pattern in DCN
  Often only one side has huge fan-in/fan-out traffic while the other side only has a few connections
    Parameter servers and workers in distributed machine learning systems
    Result-aggregators and document-lookupers in web-search back-end services
    …
    …
server
clients
Notes: In this work, we try to solve this dilemma by StaR, which offloads the network stack on RNIC, but makes the RNIC to be still stateless.
This may sound impossible at the first time. Our trick is to move the stack states to the other side.

## Slide 7: StaR overview
SQ
RQ
CQ
Conn
NIC
Host
Stateless (Server) side
Mem table
SQ
RQ
CQ
Local
Net states
Mem table
SQ
RQ
CQ
Remote
Net states
Conn
NIC
Host
Stateful (Client) side
Network
Process based on each packet
Embed server states
Receive packet/ACK
DMA or notify apps
Send packet/ACK

## Slide 8: Stateless NIC processing
Example #1
  Client SEND, Server RECV
NIC
Host
Stateless (Server) side
NIC
Host
Stateful (Client) side
Network
SQ
RQ
CQ
Conn
Mem table
SQ
RQ
CQ
Local
Net states
Mem table
SQ
RQ
CQ
Remote
Net states
Conn
App: RECV
WQEP
App: SEND
Encapsulate DMA info
Encapsulate network transmission info
Get DMA info
Get ACK header info
ACK
Data packet
CQEP

## Slide 9: Stateless NIC processing
Example #2
  Server WRITE
NIC
Host
Stateless (Server) side
NIC
Host
Stateful (Client) side
Network
SQ
RQ
CQ
Conn
Mem table
SQ
RQ
CQ
Local
Net states
Mem table
SQ
RQ
CQ
Remote
Net states
Conn
WQEP
App: WRITE
GD packet
Encapsulate DMA info
Encapsulate network transmission info
Get DMA info
Get header info
Data packet

## Slide 10: Security issue
Without any states, RNIC cannot conduct security check on received packets
  May access illegal memory address and trigger malicious traffic
Conduct security check on the client side!
Host
Host
APP
NIC
Network
Stateful (client) Side
NIC
Host
Stateless (server) side
Stateful (client) Side
Network Stack
Network Stack
APP
APP
NIC
stateless processing
Generate white list to the security module
Security Check
Security Check
Trustable packet
Trustable packet

## Slide 11: Stateless processing V.S. normal RNIC
RNIC should saturate the link bandwidth
  Both StaR RNIC and normal RNIC require a short data packet buffer to fill the pipeline
    To cover the delay of processing one packet
  However, normal RNICs require another connection state buffer
    Should be large enough to store all the connection states of those packets in the pipeline
    Consume a lot of memory when data packets are small
Connection state buffer
Packet buffer
Normal RNIC
StaR RNIC
Packet buffer
Require no connection state buffer!

## Slide 12: Performance evaluation
Preliminary simulation in NS3
Scenario #1: Stress test
  Multiple clients continuously WRITE 8B data to the server
    1 outbounding WRITE at any moment
  100Gbps link, 12us RTT, 1us PCIe latency, NIC memory of 300 conn states
160x throughput improvement
    …
Server
(Stateless)
Clients
(Stateful)
WRITE

## Slide 13: Performance evaluation
Scenario #2: RPC application
  Multiple clients continuously call the remote procedure in one server
    A 2.8KB RPC request (through SEND/RECV), and an 1.4KB RPC response (through SEND/RECV) after receiving the request.
    100Gbps link, 12us RTT, 1us PCIe latency , NIC memory of 300 conn states
4x throughput improvement
RPC request
(SEND/RECV)
RPC response
(SEND/RECV)
    …
Server
(Stateless)
Clients
(Stateful)

## Slide 14: Implementation (ongoing)
FPGA-based smart NIC
  Xilinx FPGA board
    4 SFP+ (10Gbps), PCIE3.0x8

## Slide 15: Implementation (ongoing)

## Slide 16: Wrap-up
RDMA achieves high-performance by offloading network stack on RNIC, but, states on RNIC limit its scalability
StaR makes RNIC stateless, by moving states to the other side
  Utilizing the asymmetric traffic pattern in DCN
  Track application operations (WQE) and transmission states on the other side
  Ensure security of the stateless side by controlling the traffic sent out on the stateful side
StaR RNIC breaks the scalability limitation, which may enable cooler RDMA applications

## Slide 17: Q&A Thanks!