## Slide 1: On the Impact of Cluster Configuration on RoCE Application Design
Yanfang Le
Mojtaba Malekpourshahraki
Brent Stephens
Aditya Akella
Michael M. Swift
mmalek3@uic.edu

## Slide 2: Designing and deploying high performance applications
How to design and deploy applications to have
  Low tail latency
  High throughput
  Low CPU load
Remote Direct Memory Access (RDMA)
  low latency
  high throughput and under bursty CPU load
  Ok I found it!
  RDMA 

## Slide 3: RDMA overview
RDMA cluster an applications need to be configured
Application
Application
Buffer
Buffer
Zero copy
Protocol Offload
Application
Congestion Control
Application
Congestion Control
Kernel Bypass
User
RDMA Stack
TCP/IP Stack
Kernel
HW
Application
Presentation
Session
Transport
Driver
Physical NIC
Application
Presentation
Session
Transport
Driver
Physical NIC
Copy operations
TCP/IP procedures
Offload congestion control

## Slide 4: Key question
How should I configure my RDMA cluster and application to achieve best performance?

## Slide 5: Configurations
How to transmit data?
How to handle incoming events?
Should applications be co-located?
Are NICs fair among all applications?
Can I use jumbo frames?
Design
Configurations
Deployment
Configurations
Decisions

## Slide 6: Design configurations – sending data options
Design configurations
  How to transmit data?
  How to handle incoming events?
PCIe PIO operations
RDMA data packets
DMA operations
ACKs of data packets
Pros
Cons
One network round trip regardless to the structure
Transfer just a single memory value
CPU
Mem
RNIC
Mem
READ
CPU
RNIC
Data transfer that needs two memory access (e.g., hash table)
Notes: Applications interface with the network using verbs

## Slide 7: Design configurations – sending data options
Design configurations
  How to transmit data?
  How to handle incoming events?
Pros
Cons
Only local CPU is involved
Needs multiple round trip
CPU
Mem
RNIC
Mem
READ-2
CPU
RNIC
8 B address
data
PCIe PIO operations
RDMA data packets
DMA operations
ACKs of data packets
What if network is congested?

## Slide 8: Design configurations – sending data options
Design configurations
  How to transmit data?
  How to handle incoming events?
CPU
RNIC
RNIC
CPU
WRITE
CPU
RNIC
RNIC
CPU
Send /Receive
Combine WRITE/SEND or SEND/SEND
PCIe PIO operations
RDMA data packets
DMA operations
ACKs of data packets

## Slide 9: Design configurations – sending data options
Design configurations
  How to transmit data?
  How to handle incoming events?
Pros
Cons
Only one network transfer is required
Both local and remote CPU are involved
CPU
RNIC
RNIC
CPU
UC/WRITE
UD/SEND
Compound READ
[Kalia, SIGCOMM 14']
PCIe PIO operations
RDMA data packets
DMA operations
ACKs of data packets
What if remote CPU is busy?

## Slide 10: Design configurations – Interrupt vs polling
Design configurations
  How to transmit data?
  How to handle incoming events?
Pros
Cons
No CPU overhead for detecting arrivals
Slower reaction to the arrival events
CPU
Completion Queue

## Slide 11: Design configurations – Interrupt vs polling
Design configurations
  How to transmit data?
  How to handle incoming events?
CPU
Completion Queue
CPU
Memory
Pros
Cons
Fast in reacting to a received data
CPU is busy for polling memory or CQ

## Slide 12: Configurations
How to transmit data?
How to handle incoming events?
Should applications be co-located?
Are NICs fair among all applications?
Can I use jumbo frames?
Design
Configurations
Deployment
Configurations
Decisions

## Slide 13: Deployment configurations
Deployment configurations
  Should applications be co-located?
    Applications competing on CPU
    RDMA applications competing on RNIC
  Can I use jumbo frames?
Co-located applications
$$
Separated applications
$$$$

## Slide 14: Choosing the best configuration
Each configure option has its pros and cons
There are a lot of options to configure a cluster
It is difficult to choose the best configure
We need an experiment to compare all different possible configurations

## Slide 15: Measurement goals
We evaluate RDMA performance to answer to these questions
What is the best RDMA verbs?
Should we use polling or interrupts?
What is the effect of applications competing for CPU on RDMA?
What is the effect of applications competing for RNIC on RDMA?
What is the effect of frame size on performance?
How to transmit data?
How to handle incoming events?
Should applications be co-located?
Are NICs fair among all applications?
Can I use jumbo frames?
Design
Configurations
Deployment
Configurations
Decisions
Measurements

## Slide 16: Methodology
Cloud Lab Topology
  A cluster of 17 servers
    8-core ARM Cortex-A57 processor
    64 GB of memory
    10 GbE Mellanox ConnectX-3 NIC
  Ethernet switch
    HP 45XGc
Traffic patters
  16 connections for each server
  No congestion in the switch
16 servers
Ethernet switch
Inlined message size | 256 B
Largest RDMA packet | 4 KB
Transport (WRITEs, SENDs) | Unconnected
Total experiment time | 10 seconds

## Slide 17: Methodology
Test cases
  READ-Intr
  READ-Poll
  WRITE/SEND-Poll
  SEND/SEND-Intr
  READ-Intr-
CPU
Mem
RNIC
Mem
Read-Intr
CPU
RNIC
CPU
Mem
RNIC
Mem
Read-Poll
CPU
RNIC
CPU
Mem
RNIC
Mem
Read-Intr 2
CPU
RNIC
8 B address
data
CPU
RNIC
RNIC
CPU
UC/WRITE
UD/SEND
CPU
RNIC
RNIC
CPU
SEND
SEND
WRITE/SEND-Poll
SEND/SEND-Intr

## Slide 18: What to measure?
Three scenarios
  Dedicated server for applications
  Co-located applications competing on CPU
  Co-located applications competing on RNIC
RDMA performance in the terms of
  Latency
  Throughput
What is the effect of cluster configuration on RDMA performance

## Slide 19: Which is the best verb?
Scenario I: No contention
READ-Intr
Best to fetch large values
READ-Poll
Best to fetch small values
The best verb changes when the payload size changes

## Slide 20: One side vs two side
Scenario I: No contention
WRITE/SEND-poll READ-Intr
WRITE/SEND-poll > READ-Intr
One side verbs are better

## Slide 21: Effect of RDMA verbs on throughput
Scenario I: No contention
Correct verb size depends on the size of the payload
READs faster
Similar performance
READs slower

## Slide 22: Effect of RDMA READs on throughput
Scenario I: No contention
Interrupts or polling has little impact on throughput (No CPU contention)

## Slide 23: Application needs two memory access
Scenario I: No contention
WRITE/SEND-poll < READ-Intr-2
WRITE/SEND-poll > READ-Intr-2
Best verb changes when the payload size changes

## Slide 24: Should I use jumbo frames?
Scenario I: No contention
Stable latency for small messages
READs are always better
Jumbo frames should not be used because they Increase the latency
Notes: Ways an RNIC may be loaded
  Application limited by the number of operations per second
  RNIC line-rate

## Slide 25: Effect of CPU contention on performance
  READ-poll READ-intr
READ-poll > READ-intr
CPU contention changes the best verb choice
Scenario II: CPU contention

## Slide 26: RNIC fairness among short and long messages
Scenario III: RNIC contention
Two traffic patterns (Facebook):
  Storage (4 MB)
  memcached
RNIC contention hurts the throughput of small messages for all verbs
Starve massages with small payload
Notes: While Microsoft has said that message transfers
in their RDMA deployment are often less than 4 MB
in size [26], most key-value store accesses are much smaller.
Over 90% of all values in a Facebook memcached cluster
were under 256 B

## Slide 27: Observations
Difficult to decide what is best configuration
What is the best RDMA verbs?
Should we use polling or interrupts?
What is the effect of applications competing for CPU on RDMA?
What is the effect of applications competing for RNIC on RDMA?
What is the effects of frame size on performance?
How to transmit data?
How to handle incoming events?
Should applications be co-located?
Are NICs fair among all applications?
Can I use jumbo frames?
Choosing the best performing verb is difficult
Correct choice depends on the CPU load
CPU contention changes the best verbs
RDMA applications do not fairly share the RNIC
Never use Jumbo frames because it increases latency
Design
Configurations
Deployment
Configurations
Decisions
Measurements
Results

## Slide 28: Observations
Correct verb choice depends on:
  Object size
  CPU utilization
  RNIC utilization
  The number of dependent memory accesses
Impossible for application to monitor and measure and adjust verbs
Monitor
Measure
Configure

## Slide 29: high-level library
Needs of a higher-level library
  Hide complexities from applications
  Monitor important system parameters
  Configure the verbs automatically
Application
Host Network
Monitoring
Adaptive Performance Library
CPU
RNIC
RDMA Verbs Library
Overlay Router
Application
Application
Optional
Building blocks of the library
Existing framework

## Slide 30: Conclusion
We studied
  The impact of co-located applications contending for RNIC and CPU
  The impact of large frame sizes hurt tail latency
We observed
  Correct verb choice is dependent on many variables
  It is impossible for application to monitor and measure all variables
Future work
  Implement the library
A higher-level library that hides complexities from applications is needed

## Slide 31
Thanks for the attention
Mojtaba Malekpourshahraki
Email: mmalek3@uic.edu
Website: cs.uic.edu/~mmalekpo