## Slide 1: Ether: Providing both Interactive Service and Fairness in Multi-Tenant Datacenters
Mojtaba Malekpourshahraki
Brent Stephens
Balajee Vamanan

## Slide 2: Modern datacenter
Datacenters host multiple applications with different requirements
  Memcache (delay)
  Web search (delay)
  Spark (throughput)
Datacenters host multiple competing tenants
  Private datacenters
    Example: Facebook
    Tenants  Product and applications groups
  Public datacenters
    Example: Amazon EC2, Microsoft Azure
    Tenants  Users renting virtual machines
Modern datacenters = Multiple tenants Diverse applications per tenant

## Slide 3: Network sharing
Datacenter has lots of
  Applications  Different requirements, different protocols
  Flows  different size, traffic pattern
  Tenant  same or different priority
Datacenter must meet three main requirements
How to handle this complexity?

## Slide 4: Multi-tenant datacenter requirements
Isolation among tenants
  Example: each tenant must have the fair share
Fairly share
bottleneck
Tenant 1
Tenant 2

## Slide 5: Multi-tenant datacenter requirements
Low latency for
high priority applications
Tenant 1
Tenant 2
✓
Isolation among tenants
  Example: each tenant must have the fair share
Low latency for high priority applications
  Co-located memcach and spark
  leads to a high latency

## Slide 6: Multi-tenant datacenter requirements
Isolation among tenants
  Example: each tenant must have the fair share
Low latency for high priority applications
  Co-located memcach and spark
  leads to a high latency
Utilization
  The bottleneck capacity must be
  fully utilized
How to address all of these requirements together?
Tenant 1
Tenant 2

## Slide 7: Scheduler
A scheduler could address all these network requirements
  Isolation among tenants
  Low latency for high priority applications
  Utilization
Scheduler Goals
  Implementable in limited available network resource
    Unlimited resources could do anything
  Provides a set of useful scheduling algorithm
A scheduler that achieve all these goals is hard

## Slide 8: Limitations on designing schedulers
The number of scheduling queues is limited
Two types of schedulers
  End-host based or end-to-end schedulers
  Switch based schedulers
UPS
EyeQ
AFQ
Trinity
pHost
Utopia
Sincronia
Silo
pFabric
PIAS
Slytherin
PIFO
End-hosts
In the Switches
Fastpass
PIEO
2013
2014
2015
2016
2018
2017
2019

## Slide 9: End-host schedulers
End-host
  has many queues  only at the end host doesn’t need our requirement
Shortcomings
  Waste of resource
    pHost (Sending RTS)
    Silo (Limiting burst size)
  High computational overhead
    Fastpass (Centralized)
  Slow to adapt network changes
    Trinity (ECN mark)
In switch approaches perform faster than end-to-end schedulers
EyeQ
Trinity
pHost
Utopia
Sincronia
Silo
At the End-hosts
Fastpass
2013
2014
2015
2016
2018
2017
2019
Notes: Hard to implement
  Utopia (Flow classifier)

## Slide 10: PIFO [SIGCOMM, 2016]/PIEO [SIGCOMM, 2019]
PIFO/PIEO:
  Can implement complex hierarchical programmable scheduling policies
PIFO/PIEO resources on a switch is limited (less than 100 queues)
  Cannot use PIFO to implement the full scheduling policies in switches
  You cannot have all possible scheduler
  The number of required queues increases with the number of traffic class
UPS
AFQ
pFabric
PIAS
Slytherin
PIFO
In the Switches
PIEO
2013
2014
2015
2016
2018
2017
2019

## Slide 11: Key question!
Ether
Can we implement a useful set of scheduling policies within
the constant number of scheduling queues?

## Slide 12: Ether overview
Contributions
  Decoupling fair queueing (fairness) from priority queue (FCT)
  Variety of scheduling
    Fair queueing, Priority queue, SJF, LSTF
    Any combination of them
  Ether requires a fixed number of scheduling queues
Implementation:
  the implementation of two-sided-queue in programmable switches
Key insight:
  Trade-off fairness in short time intervals in bounded intervals
  Steal capacity from a tenant in short period of times to optimize tail FCT in others

## Slide 13: Outline
Datacenter network
Existing proposals
Design
  Ether High level
  Design potential
Results

## Slide 14: Ether framework
Ether uses two set of queues and two hashing functions
Queue operations
  Enqueue
  Dequeue
Fairness optimizer
Tail optimizer
Priority
  Dequeue
  based on
  the priority
  Enqueue
  based on
Enqueue
based on
Packet
Priority
Packet Fromat

## Slide 15: Ether framework – fairness optimizer
Fairness optimizer
  In each round, bytes dequeue from fairness to tail optimizer
  is the smallest nonzero queue length
  Packets distributes to any of 𝑛 queues in fairness
Fairness optimizer
Tail optimizer
6
1
9
0
2
Priority
Window

## Slide 16: Ether framework – tail optimizer
Tail optimizer
  Enqueue packets based on the flow ID,
  Dequeue the packets based on their priority
  Priority is slack time
Fairness optimizer
Tail optimizer
6
1
9
0
2
Priority

## Slide 17: How it works?
Two tenants
  Tenant 1 (Memcached, Websearch)
  Tenant 2 (Spark)
Fairness optimizer
Tenant 1
Tenant 2
Tail optimizer
1
9
0
2
Priority
Window
Spark < Memcached < Websearch

## Slide 18: How it works?
Two tenants
  Tenant 1 (Memcached, Websearch)
  Tenant 2 (Spark)
The window is important in accuracy of approximation
Fairness optimizer
Tail optimizer
9
0
1
Priority
Tenant 1
Tenant 2
Ether
Fairness
Order of dequeuer is different
Window
Spark < Memcached < Websearch

## Slide 19: Discussion – windowing limits
Some tenants generate few packets
  Issue: adversely affect the tail optimization
  Reason: few packets in the tail optimizer
  Solution: limit minimum window size ()
All tenants generates too many packets
  Issue: too many flows in the window
  Reason: Too many hash collisions for flows
  Solution: limit maximum window size ()
Best window size:
4 packets only
low efficiency FCT optimization
Collisions in hashing flow id
(5 queues in the next stage)
Priority
Priority
✓
controls FCT performance
controls collisions on the FCT optimizer
and the number of queues in FCT optimizer

## Slide 20: Outline
Datacenter network
Existing proposals
Design
  Ether High level
  Design potential
Results

## Slide 21: Ether with Programmable Switches
Programmable switches
  There is no two layers of queues
Solution:
  Divide the queue space in to two
  Use different hashing functions
  Implement two layers of switches using packet resubmit
Implement a two steps of multilevel queue using PSA
Ingress Parser
Ingress Parser
Ingress Parser
Ingress Parser
Update
Sketch
<
Resubmit packet
Dequeue In line rate
>
Notes: Programmable switches are designed to work in line rate for minimum packet size
1) We think that under normal line rate we could get max throughput
2) We use the direct submit and a sketch to remove the need of resubmit

## Slide 22: Discussion
LSTF
LSTF + WFQ
WFQ
SJF
Strict Priority
LSTF + WFQ + Strict Priority
Ether could provide a set of scheduling algorithms

## Slide 23: Evaluation
Goals
  Can Ether achieve fairness among all tenant and improve the FCT per tenant?
How Ether works compared to
  Ideal fair queuing (FQ)
  Ideal FCT optimizer (pFabric)
Measured parameters
  Jain’s index fairness
  99 percentile tail flow completion time

## Slide 24: Methodology
Network simulator (ns-3 v3.28)
  Workloads
  Parameters
10 Gbps
400 Hosts
10 Spine Switches
20 Leaf Switches
Short flows | 8 - 32 KB
Long flows | 1 MB
Number of tenants | 10
 | 1
 | 570(pkt)
 | 1
 | 570(pkt)
Topology

## Slide 25: Fairness and FCT
Ether outperforms pFabric’s fairness by 18%, Ether outperforms FQ tail FCT by 25%
Notes:   For loads higher than 60%, pFabric’s fairness suffers by about 20%
  Ether achieves better fairness than pFabric. Specifically, Ether achieves similar fairness as ideal (within 5%) and outperforms pFabric by about 18% (JFI of 0.95 for Ether vs. 0.8 for pFabric).

## Slide 26: Sensitivity to number of queues
For the workload we evaluated, the number of required queues between 24 to 32
FCT converges
Variable
fairness optimizer
FCT optimizer
Fixed = 16
Fixed = 16
fairness optimizer
FCT optimizer
Variable

## Slide 27: Conclusion
We proposed Ether
  Ensuring fairness over longer timescales
  Provide short tail FCT over shorter timescales
We observed that Ether
  Ether outperforms pFabric’s fairness by 18%
  Ether outperforms FQ tail FCT by 25%
Future work:
  Implement Ether on programmable switches
  Generalize the architecture to support other scheduler types
  Generalize the architecture to support hierarchy

## Slide 28
Thanks for the attention
Mojtaba Malekpourshahraki
Email: mmalek3@uic.edu
Website: cs.uic.edu/~mmalekpo